## Slide 1
Fermentation Kinetics
The study of rates in microbial growth and product formation

## Slide 2
The Big Picture
Cell Growth
How microbial populations increase over time
Substrate Consumption
How food sources like glucose are utilized
Product Formation
How desired metabolites are produced
By-product Formation
How waste products are generated
Mathematical framework to optimize and control industrial fermentations for maximum yield and productivity.

## Slide 3
Monod Kinetics
The most famous model describing microbial growth rate as a function of limiting nutrient concentration

## Slide 4
The Monod Equation
μ (mu)
Specific growth rate (h⁻¹) - rate of cell division per unit biomass
μmax
Maximum specific growth rate when nutrients are abundant
[S]
Concentration of limiting substrate (e.g., glucose g/L)
Ks
Saturation constant - substrate concentration at μ = ½μ_max

## Slide 5
Growth Rate Behavior
Low Substrate [S] << Ks
Growth rate is very small, microbes grow slowly.
High Substrate [S] >> Ks
Growth rate approaches μmax (saturation).

## Slide 6
Thermal Kinetics
How temperature affects biochemical reaction rates in fermentation

## Slide 7
The Arrhenius Equation
01
Rate Constant (k)
Could be μmax from Monod equation
02
Pre-exponential Factor (A)
Frequency factor for molecular collisions
03
Activation Energy (Ea)
Energy barrier reactions must overcome
04
Temperature (T)
Absolute temperature in Kelvin
Ea (activation energy) = how sensitive microbial growth is to temperature.
Low Ea → growth not very sensitive to temperature.
High Ea → small temperature change causes big changes in μmax

## Slide 8
Temperature Effects on Fermentation
Growth Rate Increase
μ_max increases with temperature up to optimum point
Cell Death Risk
High temperatures dramatically increase thermal death rate
Enzyme Denaturation
Excessive heat unfolds enzymes, rendering them inactive
Each microorganism has an optimal temperature range for maximum efficiency.

## Slide 9
Engineering Integration
Thermal Kinetics
Control bioreactor temperature
Monod Parameters
Define μmax and growth rates
Fermentation Model
Design and operate process
Biochemical engineers use this integrated approach to optimize industrial fermentation processes for maximum productivity and yield.